## Slide 1: Instruction Set

## Slide 2: Instruction Set
In computer architecture, an instruction set, or Instruction Set Architecture (ISA), is the complete collection of commands that a central processing unit (CPU) can understand and execute.
It serves as the fundamental interface between a computer's hardware and software.
The code is usually in 1s and 0s, or machine language. It contains instructions or tasks that control the movement of bits and bytes within the processor.

## Slide 3
Example of some instruction sets ?
ADD ? Add two numbers together.
JUMP ? Jump to designated RAM address.
LOAD ? Load information from RAM to the CPU.

## Slide 4: Components of an instruction
Each instruction within the set is a statement in machine language, composed of two main parts:
Opcode (Operation Code): This specifies the action or operation to be performed, such as ADD, MOVE, or JUMP.
Operand(s): These are the data or memory addresses on which the opcode will operate. For example, in an instruction like
ADD R1, R2
ADD is the opcode, and R1 and R2 are the operands.

## Slide 5: Types of instruction set architectures
Instruction sets are broadly categorized based on their complexity, which influences the CPU's design and performance characteristics
Reduced Instruction Set Computer (RISC)
Complex Instruction Set Computer (CISC)

## Slide 6: Reduced Instruction Set Computer (RISC)
A number of computer designers recommended that computers use fewer instructions with simple constructs so that they can be executed much faster within the CPU without having to use memory as often. This type of computer is called a Reduced Instruction Set Computer.
RISC architecture uses a small, highly optimized set of simple instructions, most of which execute in a single clock cycle.

## Slide 7: Key characteristics: RISC
  Fewer and simpler instructions.
  Emphasis on software optimization.
  Extensive use of processor registers.
  Load/Store architecture, where memory access is restricted to dedicated load and store instructions.
  Easier to implement pipelining, a technique that improves instruction throughput.
Examples:
ARM (used in most mobile devices) developed by Arm Holdings
SPARC( Scalable Processor Architecture)

## Slide 8: Complex Instruction Set Computer (CISC)
CISC is a computer where a single instruction can perform numerous low-level operations like a load from memory and a store from memory together.
CISC architecture uses a large set of complex, multi-step instructions.
The CISC attempts to minimize the number of instructions per program but at the cost of an increase in the number of cycles per instruction.

## Slide 9: Key characteristics:CISC
  More instructions and complex addressing modes.
  Emphasis on hardware optimization, with complex operations built directly into the processor.
  Variable-length instructions that can take multiple clock cycles to complete.
  Less frequent use of registers compared to RISC.
Examples: The x86 architecture used in Intel and AMD processors