## Slide 1: Input-Output and Interrupt

## Slide 2: Input-Output and Interrupt
In computer architecture, Input/Output (I/O) refers to the communication between a computer system and the outside world, while interrupts are the mechanism that efficiently manages this communication.

## Slide 3: Input and output (I/O)
Input is the data a computer receives, and output is the data it sends. An I/O interface connects the Central Processing Unit (CPU) and memory to external devices, such as keyboards, monitors, and storage drives.
Input devices
Definition: Hardware that allows a user or another system to send data to a computer.
Examples: Keyboard, mouse, microphone, and scanner.
Process: When an input device is used, it generates a signal. For example, pressing a key on a keyboard sends an 8-bit alphanumeric code to a special input register, where it waits to be processed by the CPU.

## Slide 4: Input and output (I/O)
Output devices
Definition: Hardware that displays or delivers the results of processed data from a computer.
Examples: Monitor, printer, and speakers.
Process: The CPU sends processed data to a special output register, which then transfers the data to the output device. For example, the output register holds the data for a printer until the device is ready to print the corresponding character.

## Slide 5: The I/O problem
The CPU and memory operate at a much faster rate than most I/O devices. This speed mismatch creates a bottleneck, as the CPU must wait for slower devices to complete their tasks. There are two main ways to handle this:
Programmed I/O: The CPU constantly checks (or polls) the status of an I/O device to see if it is ready for a data transfer. This is simple to program but is highly inefficient because it wastes CPU cycles.
Interrupt-driven I/O: The more efficient solution, where the I/O device interrupts the CPU only when it is ready. This allows the CPU to perform other tasks while waiting for the I/O operation to finish.

## Slide 6: Interrupts
An interrupt is a signal that temporarily stops the CPU's current process to handle an urgent task, such as a data transfer from an I/O device.
How interrupts work
Interrupt signal: An I/O device, like a keyboard, signals the CPU with an interrupt request when new data is available.
Save state: The CPU saves the current state of the program it was running. This includes storing the contents of the program counter and other registers onto a memory stack.
Interrupt service routine (ISR): The CPU jumps to a specific set of instructions, known as the interrupt service routine, to handle the I/O request.
Restore state: After the ISR is complete, the CPU retrieves the saved state from the stack and resumes the interrupted program exactly where it left off.

## Slide 7: Types of interrupts
Hardware interrupts: Generated by external devices or I/O modules, often to signal that a task is complete or that data is ready.
Software interrupts: Generated by program instructions. These can be intentional system calls or unexpected exceptions, like a "divide by zero" error.
Timer interrupts: Generated by a timer within the processor at regular intervals. This allows the operating system to perform tasks periodically.
Direct Memory Access (DMA): A highly efficient method that uses a special DMA controller to manage high-speed data transfers directly between memory and an I/O device, without continuous CPU involvement. The CPU is only needed to initiate the transfer and is notified with an interrupt when the transfer is complete.